## Slide 1: Thermogravimetric Analyzer
TGA measures a sample's weight as it is heated or cooled in a furnace
Working Principle
TGA
To determine the composition and decomposition behavior of complex materials, thermal stability analysis
Application
TGA and DTG graph for sodium bentonite

## Slide 2: Differential Scanning Calorimeter
Measures enthalpy change of sample as a function of temperature
Working Principle
DSC Instrument
Used to identify polymer and its properties
Determination of thermodynamic and thermophysical properties
Application
OIT response of HDPE

## Slide 3: Fourier Transform Infrared Spectrometer
The chemical bonds present in the material absorbs the infrared radiation at corresponding wavelength.
Working Principle
FTIR instrument
To qualitatively determine chemical composition of materials
Forensic analysis, quality control and assurance.
Application
FTIR spectra of lime stabilised soils

## Slide 4: Helium Gas Pycnometer
Solid volume is measured by employing gas displacement as per Boyle’s law.
Working Principle
To accurately measure the volume of solids and true density.
Application
Helium gas pycnometer

## Slide 5: Gas Chromatography
GC is used for qualitative and quantitative analysis of compounds that can be vaporized without decomposition.
Application
Agilent gas chromatograph (GC) 7890A
In gas chromatography (GC), the mobile phase is a carrier gas. The stationary phase is a polymer on an inert solid support. The gaseous compounds being analyzed interact with the walls of the column, which is coated with a stationary phase. This causes each compound to elute at a different time, known as the retention time of the compound.
Gas tight syringe for gas injection
Working Principle

## Slide 6: UV Visible Spectrophotometer
The absorption of ultraviolet light or visible light by chemical compounds results in the production of a distinct spectra.
Working Principle
UV-Visible spectrophotometer
Quantification of specific substances and aggregate parameters in water and wastewater, quantitative determination of transition metal ions, organic compounds, and biological macromolecules
Application

## Slide 7: Atomic Absorption Spectrometer
AAS measures the concentration of elements in a liquid sample based on energy absorbed from certain wavelengths of light
Working Principle
AAS instrument
To quantify the elements in a solution.
To detect trace amounts of harmful chemicals in water samples
Application

## Slide 8: Water Quality Analyzer
Water quality standards are measured using an electrode after suitable calibration with the standards
Working Principle
Water Quality Analyzer
Measurement of pH, electrical conductivity and total dissolved solids
Application

## Slide 9: iSorb-HP
A known amount of gas is allowed to expand into a sealed container with sorbent. The amount of gas adsorbed can be calculated from the mass balance equation, provided the void volume of sorbent is known.
Working Principle
iSorb-HP
To determine the adsorption-desorption isotherms and kinetics for gases over a wide range of pressures (upto 200 bar) and temperatures(upto 400°C).
Application
CO2 adsorption isotherm on F400

## Slide 10: AutoSorb
Extended- range opore size and surface area analysis using appropriate adsorbate is made by high vacuum, oil free turbomolecular system and high precision low pressure transducers
Working Principle
Representative Image of AutoSorb Equipment, Yet to Install)
BET surface area, TPD, TPR.
Application

## Slide 11: Accelerated UV Weatherometer
Simulates field exposure conditions in a landfill using fluorescent UV and condensation weathering methods
Working Principle
UV weatherometer
To study the longevity of geomembranes subjected to accelerated UV ageing
Application

## Slide 12: Accelerated Xenon Arc Weatherometer
Simulates field weathering conditions using xenon arc lamps and condensation techniques
Working Principle
Xenon Arc weatherometer
To study the longevity of geomembranes subjected to accelerated UV ageing
Application

## Slide 13: Melt Flow Index
Measures the rate of extrusion of molten polymer at specified conditions
Working Principle
Melt Flow Index
Indicative of molecular weight, quality control
Application

## Slide 14: Geomembrane Dog Bone Cutter
To cut the geomembrane into a dog bone shaped sample
Working Principle
Dog Bone cutter
To assess the tensile strength, crack resistance of geomembranes
Application

## Slide 15: Research Centrifuge
The radial acceleration causes denser particles to settle to the bottom of the tube, while low-density substances rise to the top
Working Principle
Research Centrifuge
Separation of mixtures with close densities,separate immiscible liquids, suspended solids and insoluble particles
Application

## Slide 16: Geotechnical Centrifuge
Centrifugal acceleration to simulate increased gravitational acceleration
Working Principle
Geotechnical centrifuge
Used for testing physical scale models of geotechnical engineering systems
Application

## Slide 17: Flexible-wall Permeameter
Controls the effective stress conditions and degree of saturation by back-pressure application, and prevention of side-wall leakage during permeation via use of a latex membrane in close contact with the specimen
Working Principle
Flexible wall permeameter
Measurement of hydraulic conductivity of saturated porous material
Application

## Slide 18: Sieve Shaker
A sieve shaker separates particles by passing them through a sieves and agitating the sample in order to obtain complete separation.
Working Principle
Sieve shaker
To assess the particle size distribution of granular materials
Application

## Slide 19: Time Domain Reflectometer
TDR sensors use parallel rods, acting as transmission lines. A voltage is applied to the rods and reflected back to the sensor for analysis. The speed or velocity of the voltage pulse along the rod is related to the apparent permittivity of the substrate
Working Principle
Determination of soil moisture content, rate of infiltration.
Application
Time domain deflectometer

## Slide 20: Fabricated Diffusion Cells
The concentration gradient between the source and receptor cell drives the contaminant by a process called diffusion
Working Principle
Aqueous phase
Determination of diffusion coefficient of VOCs in both aqueous and vapor phase
Application
Vapour phase

## Slide 21: Fabricated Carbon dioxide Diffusion cells
The carbon dioxide sensors kept at the source and receiver end measures the variation in the concentration of gas and hence the rate of diffusion
Working Principle
To estimate the coefficient of carbon dioxide gas diffusion through a compacted geomaterial
Application
Carbon dioxide diffusion measurement