## Slide 1
Retrofitting of RCC structure of new cooling tower,
IOCL Gujarat Refinery
CE 5120 Maintenance and Rehabilitation of Constructed Facilities
Course Project on
Images are sourced from internet for illustration purpose
Anupama V. A.
CE19D034
Nilakanmani Manimaran
CE19D038
Ramakrishna S.
CE19D033

## Slide 2
OVERVIEW
References
Expected outcomes
Schedule
Objectives
Assumptions
Problem Identification
Project Introduction

## Slide 3
INTRODUCTION
a
c
b
Founded: 1966
Owner: IOCL
Operating units: 40
Capacity: 13.7 MMT per year
COOLING TOWER
FRP/RCC
Susceptibility to reinforcement corrosion

## Slide 4
PROBLEM
The representative photographs of corrosion in cooling tower
Biological growth in cooling tower
Exposed corroded rebars, cracks, spalling, delamination and biological growth

## Slide 5
ASSUMPTIONS
Site Conditions
  Coordinates:
    22°22'13.80"N 73°07'31.80"E
  Nearest city: Vadodara
  Humidity: 60%
  Temperature: 15°C - 35°C
  Proximity to coast: 30 km
Construction
  Grade of concrete:
    M25(columns, shells)
      M20 (other members)
  Rebars: CTD bars
  Cover depth: 25 mm
  Pile foundation
  Water source: Mahi river
Cooling Tower
  Type: Natural draught
  Material: RCC
  Filler material: Polypropylene (63 mm x 63 mm, 9MFI)
  Supply Voltage: 380 V
  Supply Phase: Three phase
Problems
  Early age cracks
  Fresh water leaching
  Carbonation (suitable humidity, higher atmospheric concentration of CO2 and high local Temperature)
  High TDS in recirculating water
  Biological growth

## Slide 6
OBJECTIVES
Recommend condition assessment procedure to identify the root cause of distress and extent of damage
Develop repair and retrofitting strategies for the structural elements of a heavily corroding cooling tower
Revise the tender specification with durability design to achieve the target service life

## Slide 7
SCHEDULE

## Slide 8
OUTCOMES
The primary outcome is to recommend tender specification, which can ensure the structure to achieve its targeted service life after repair
The other outcomes are
Revised tender specification including strength and durability approach
Repair methodology and preventive maintenance strategy
Extended corrosion-free initiation phase and enhanced service life
Ensured safety, functionality and aesthetics of the structure

## Slide 9
REFERENCES
https://spxcooling.com/wp-content/uploads/AE-SK-18.pdf
https://www.indiamart.com/proddetail/rcc-cooling-tower-4823753530.html
https://www.oilandgasproductnews.com/article/28534
http://spxcooling.com/wp-content/uploads/Cooling-Tower-Fundamentals.pdf
https://iocl.com/AboutUs/GujaratRefinery.aspx
Tender documents for Retrofitting of RCC structure of TPS new cooling tower at Gujarat Refinery.

## Slide 10
THANK YOU