## Slide 1: Surface Wave Testing
The wavefield radiated by seismic tremors contains surface waves which are dispersive in nature.
Working Principle
Dispersive properties of Rayleigh wave is used in Multichannel Analysis of Surface Wave (MASW) to obtain the subsurface's shear wave velocity profile.
Application
Surface wave testing
Numerical simulation of wavefield

## Slide 2: Geophones
The geophone’s magnetic core and coil system converts the ground motion into electrical voltage.
Working Principle
Used to measure low frequency vertical as well as horizontal ground motion. Usually an array of 24-48 geophones is used in multichannel analysis.
Application
4.5 Hz geophones
24 Channel receiver array

## Slide 3: Data Acquisition System
Collect and store multichannel receiver signal.
Working Principle
Converts the analog signal to a discrete digital signal with a very high sampling rate and stores the common shot gather.
Application
24 channel DAQ system
Multichannel shot gather

## Slide 4: Analysis tools
Mathematical wavefield transformation tools decompose the recorded data into their frequency-dependent phase velocities.
Working Principle
Used to obtain a high-resolution multimodal field dispersion image that will act as a reference in inverse analysis.
Application
Multimodal dispersion graph
Shear wave velocity profile